## Slide 2: Fairness
If all honest validators see transaction a before transaction, then a ust be in an earlier or the same block as b.
There’s some issues with that definition (e.g.,we cannot guarantee termination), we’ll ignore that for the moment.

## Slide 3: Basic Wendy
When a validator sees a transaction, it adds a sequence number and sends a vote for that transaction/sequence number to all validators
We call a transaction a preferred over b if, by the rules of fairness, it needs to be in an earlier or the same block
A validator collects votes and decides to delay some TXs from being passed to the blockchain. A transaction is blocked if
It is possible for a currently unknown transaction to be preferred; this is because an insufficient votes has arrived
A transaction is preferred that is already blocked.

## Slide 4: Basic Wendy (2)
With more incoming votes, every transaction will get sufficient votes to not be blocked due to a possibly unknown transaction. It will then unblock itself and all other transactions blocked by it.
A transaction tx is blocked (by a so far unknown one) if it got less than t+1 votes. Once t+1 votes (in sequence) have arrived, no unseen transaction can have n-t votes preceeding tx.
A transaction tx1 is not blocked by another tx2, if t+1 parties reported having seen tx1 before tx2.
A vote from a validator is blocked is there is a vote with a lower sequence number missing.

## Slide 5: Implementation
Wendy has two core parts:
  The recompute function reevaluates which current transactions are blocked. To this end, for each active transaction, a set of transactions preferred over it (B) it is computed. If any transaction in that B is blocked due to insufficient votes, the transaction itself is blocked. Unblocked transactions are moved from the active bugger U to the blockchain buffer Q. This function calls two functions, is_blocked and is_blocked_by, which essentially define what fairness is.
  The processMessage function evaluates incoming transactions and votes, cleans the buffers once a block has been delivered in the blockchain. It also makes sure that votes that come out of sequence are buffered and processed once their time has come.

## Slide 6: Performance
Wendy runs parallel to the blockchain, and in that does not add latency. She does, however, delay transactions to later blocks.
Transactions that don’t need fairness can be passed through and suffer no delay
Three factors
  Insufficient votes: A transaction cannot be processed yet as there aren’t enough votes on it to know if it can be scheduled
  Blocking: A transaction needs to be in the same block as one of the above category
  Out of order votes: Voting messages are overtaking each other; Wendy needs to see a full sequence and thus needs to wait for the faster one

## Slide 7: First Measurements
Insufficient votes depends directly on the ratio message-delivery time/block-creation time. The number of TXs delayed there is pretty much exactly that ratio
Blocked TXs added another ~15-30% of those in our simulations.
  Variation of the speed in which transactions arrive at validators
  Number of TXs blocked by above reason
  Above ratio, as many conflicts are resolved before the next block is ready
In a halfway normal network, vote overtaking had no impact. If me model erratic behavior (adding a multiple of the normal message delivery time at random), we saw a larger number of messages affected (add graph) ?